## Slide 1: Aircraft Lateral Flight Optimization Using Artificial Bees Colony
Alejandro Murrieta-Mendoza, Audric Bunel, Ruxandra M. Botez
Université du Québec / ÉTS/ LARCASE

## Slide 2: Motivation
Airline Expenses: 26%
www.ucalgary.ca
Aeronautical Industry CO2 production:
2%

## Slide 3: Motivation
Canada:
The Green Aviation Research & Development Network (GARDN)
      Develop technologies to reduce aircraft noise and emissions.
        Governmental Funding + Industrial Funding + University Expertise

## Slide 4: Introduction
Two types of reference trajectory
  1.-Typical Vertical Navigation:
VNAV

## Slide 5: Introduction
      2.- Lateral Reference Navigation (LNAV)

## Slide 6: Objectives
    Find the combinations of waypoints that reduce the fuel requirements .
    Reduce emissions caused by fuel burn.
    Reduce the flight cost
    Explore the Artificial Bees Colony Algorithm Potential

## Slide 7: Trajectory Studied
Cruise Phase
  Montreal - Paris
Constant Altitude
Fixed Mach number

## Slide 8: Methodology
Flight Cost

## Slide 9: Methodology
Performance Database
Flight Mode | Inputs | Output
Cruise | Mach Gross weight (kg) ISA deviation temperature (C) Altitude (ft) | Fuel flow (kg/hr)

## Slide 10: Methodology
Ant Algorithm
  Ants wander around for food sources.
  Different ants find the same food source.
  Over time the shortest path is selected.
  Use pheromone to keep track of the path
    The more ants are in a path, the more pheromone there is

## Slide 11: Methodology
Flight time
  Flight Speed

## Slide 12: Methodology

## Slide 13: Methodology
Bees!
  Working Bees: Exploit known food sources.
  Onlooker Bees: Exploit the best food sources.
  Scout Bees: Look for new food sources.
  Food Source = A given trajectory

## Slide 14: Methodology
Step 1: Initialization
  Generate Random Trajectories.
  Assign Every Trajectory to a Different Working Bee.
Step 2: “Working Bees”
  Mutate the given trajectory
    Random waypoint is selected and its trajectory is changed.
    Better trajectory found? Replace the old one.
    Mutation failed? Keep count!

## Slide 15: Methodology
Step 3: On-looker bee.
  Every Trajectory is Rated by its Fitness.
  The most promising trajectories are selected.
  The selected trajectories are mutated as the working bees do.
Step 4: Scout Bee
  Maximal counting number: Discard the trajectory
    It is the optimal!! – Doesn`t matter it is already stored.
  Create a new one. Assign it to a working bee

## Slide 16: Methodology
Step 5: When do we stop?
  Maximal number of iterations.

## Slide 17: Results
Montreal to Paris
  2970 nm
  36 waypoints
  Mach number constant
  Fixed flight level.

## Slide 18: Results
Trajectories
  Green: Optimal Candidates
  Black: Reference
  Blue: Limits
  Red: Optimal

## Slide 19: Results

## Slide 20: Results
Fuel burn savings:
  102 kg – 140kg

## Slide 21: Conclusion
The ABC algorithm was able to find better routes than the reference.
Flight cost was reduced.
Reduction depends on weather
More flights are required to measure the real impact.

## Slide 22: Thank You
Q & A